## Slide 1: Energy Conservation in Residential Building
Decision Analysis
BLDG 6581
Instructor Dr. T. Stathopoulos
Group Members
Gianina Martinez
Vivekkumar Chatrola
Nishit Jagdishkumar Kadia
Mohammad Mehmood Syed

## Slide 2
ENERGY EFFICIENCY DESIGNS ON RESIDENTIALS BUILDINGS
USING MOTION SENSING LIGHTS
USING SOLAR WALLS
CHOSING THE BEST DESICION TO DECREASE A RESIDENCIAL BUILDING’S ENERGY CONSUMPTION

## Slide 3: 1. Lifetime of this project = 30 years 2. Natural gas price, fixed rate = $0.55/m 3 3. Price of electricity = $0.05/kwh 4. Interest rate = 4%
GENERAL PARAMETERS

## Slide 4
DECISION TREE

## Slide 5
SolarWall is used to substitute the building heating system
It captures the heat from the sun as passes it to the building ventilation system
Cost of the Solar Wall as per manufacturer is $285/m2 (included the cost of installation, material and labor)
Heating obtained from SolarWall is calculated to m3 of natural gas saved per m2 of SolarWall.
Thus to calculate annual savings:
Annual Savings = Size Solar Wall (m2) x Price Natural Gas ($/m3) x Efficiency (m3/m2)
SOLARWALLS

## Slide 6
SOLARWALLS
SolarWall System

## Slide 7
SOLAR WALLS

## Slide 8
DECISION TREE
DECISION TREE
(SOLARWALLS)

## Slide 9
LARGE PANEL
The calculation of Net Present Worth is carried as under:
NPW = PV (rate, years, annual savings) - (Initial Cost + Govt. Benefits)
The calculation of EMV for NPW = $82,779.63
While the EMV for ROR = 10.75%

## Slide 10
SMALL PANEL
The calculation of Net Present Worth is carried as under:
NPW = PV (rate, years, annual savings) - (Initial Cost + Govt. Benefits)
The calculation of EMV for NPW = $76,784.69
While the EMV for ROR = 15.10%

## Slide 11: Sensitivity Analysis:
A Sensitivity analysis for SolarWall is carried out to find out the variations that can happen in the NPW with the variations in the efficiency of the panel
The variation of +20% for each case of High and Low efficiency.

## Slide 12: Preposterior Analysis
The cost of the test is $2000.
The probability table obtained from the effectiveness of the test is shown as under:
The level of uncertainty is due to the changing weather conditions, but the better probabilities are obtained because of factoring the certainty of the location.

## Slide 13: Preposterior Analysis
The final EMV of the test alternative is obtained as, EMV(test) = $81,036
the Rate of Return(test) = 14.35%
According to the EMV the preference is obtained as
$82,779.63 > $81,036 > $76,784.89
Large Panel ≻ Test Alternative ≻ Small Panel

## Slide 14: Value of Information
Value of Information is calculated as:
VI = EMV(T) – EMV(a*)
VI = $81,036 - $82,779.63
VI = -$1,743.63
Thus, the test is not justified.

## Slide 15
DECISION TREE
DECISION TREE
(MOTION S LIGHTS)

## Slide 16
MOTION SENSING LIGHTS

## Slide 17
MOTION SENSING LIGHTS (100 W)
No. of hours convention lights used in a year
=No. Floors * Lights each/floor * Hours per day * Days per year 14x10x24x365= 1226400 hr/yr

## Slide 18
MOTION SENSING LIGHTS
100 WATTS Lights

## Slide 19
MOTION SENSING LIGHTS (60 W)
= No. of floors * Lights in each floor * No. of apartments in each floor * No. of time turned on * seconds it stays on * Days per year / 3600

## Slide 20
MOTION SENSING LIGHTS
60 WATTS Lights

## Slide 21
UTILITY CRITERION
U($50k) =0.4*1=0.4
U($30k) =0.4*0.4=0.16
U($80k) =0.4*1.0+0.6*0.4=0.64
U($120k) =0.4*1+0.6*0.64=0.784
U($150k) =0.4*1+0.6*0.784=0.87

## Slide 22
DECISION TREE
UTILITY CRITERION
NPW | U(G) | U(M) | U(V) | U(N)
173000 | 1 | 1 | 1 | 1
170000 |  |  |  | 
165000 |  |  |  | 
160000 | 0.98 |  |  | 
155000 |  |  | 0.784 | 
150000 |  | 0.87 |  | 0.784
145000 | 0.97 |  |  | 
140000 |  |  |  | 
135000 |  |  | 0.64 | 
130000 |  |  |  | 0.64
125000 | 0.95 |  |  | 
120000 |  | 0.784 |  | 
115000 |  |  |  | 
110000 |  |  |  | 
105000 | 0.92 |  |  | 
100000 |  |  | 0.4 | 
95000 | 0.87 |  |  | 
90000 |  |  |  | 
85000 |  |  |  | 0.4
80000 | 0.78 | 0.64 |  | 
75000 |  |  |  | 
70000 | 0.64 |  |  | 
65000 |  |  | 0.16 | 
60000 |  |  |  | 
55000 | 0.4 |  |  | 
50000 |  | 0.4 |  | 0.16
45000 |  |  | 0.064 | 
40000 |  |  |  | 
35000 |  |  |  | 0.064
30000 | 0.16 | 0.16 |  | 
25000 |  |  |  | 
20000 | 0 | 0 | 0 | 0
 | y = -6E-11x2 + 2E-05x - 0.3478 | y = 0.4527ln(x) - 4.4933 | y = 2E-11x2 + 2E-06x - 0.0589 | y = 6E-06x -0.1513
 | R² = 0.9906 | R² = 0.9962 | R² = 0.9977 | R² = 0.9944
The utility values for the range of monetary values from $20 to $173K have been determined

## Slide 23: A Utility function of money (NPW)
Chart: Utility Graphs
| 173000 | 170000 | 165000 | 160000 | 155000 | 150000 | 145000 | 140000 | 135000 | 130000 | 125000 | 120000 | 115000 | 110000 | 105000 | 100000 | 95000 | 90000 | 85000 | 80000 | 75000 | 70000 | 65000 | 60000 | 55000 | 50000 | 45000 | 40000 | 35000 | 30000 | 25000 | 20000
U(G) | 1 | 0.98 | 0.97 | 0.95 | 0.92 | 0.87 | 0.78 | 0.64 | 0.4 | 0.16 | 0
U(M) | 1 | 0.87 | 0.784 | 0.64 | 0.4 | 0.16 | 0
U(V) | 1 | 0.784 | 0.64 | 0.4 | 0.16 | 0.064 | 0
U(N) | 1 | 0.784 | 0.64 | 0.4 | 0.16 | 0.064 | 0
A Utility function of money (NPW)

## Slide 24: Utility Values for SolarWall
Equation y = (6*10-6x) – (0.1513) associated with Utility(N) is used to obtain utility values of various SolarWall alternatives in consideration as under
Large Panel (Direct Installation) ≻ Test Alternative

## Slide 25: Utility Values for Motion Sensing Lights
Equation y = (6*10-6x) – (0.1513) associated with Utility(N) is used to obtain utility values of Motion Sensing Lights alternatives in consideration as under
100W Motion Sensing Lights ≻ 60W Motion Sensing Lights
100W Motion Sensing Lights ≻ Large Panel (Direct Installation)

## Slide 26
MULTIPLE OBJETIVE ANALYSIS
Considering the conditions of the project, four objectives are decided to be considered as follows:
• Net Present Worth (NPW) - A
• Rate of Return - B
• Convenience to Tenants - C
• Chance of Successful Implementation – D
The weights to each of the parameters are given as under:

## Slide 27
MULTIPLE OBJETIVE ANALYSIS
The table below shows the probabilities for the Multi-Objective parameters
The results are obtained as under

## Slide 28: Conclusion
Based on prior analysis of the SolarWall alternative large panels should be installed instead of small panels when compared using Net Present Worth.
While the independent analysis for the two alternatives of Motion Sensing Light shows that the NPW of 100W option yields higher NPW
according the Expected Monetary Value (EMV) the criteria of 100W is most preferred
Also, NPW has been obtained using the Utility theory
Motion Sensing Light of 100W has higher EUV then the best alternative of SolarWall
Finally, Multiple objective analysis has been carried and according to it alternative of 100W motion sensing light must be preferred

## Slide 29: Thank You